FSU DAC QUALITY EVALUATION FLAGS

A description of FSU DAC quality evaluation flags. A more detailed description of the quality evaluation process can be found at: http://www.coaps.fsu.edu/woce/docs/qchbook/qchbook.htm

The quality control flags are single alphabetic characters for each data value. Only those variables with a qcindex in the original one-minute data files have flag values (the qcindex is an integer pointer to the flag for a selected variable), i.e. not all meteorological variables are quality controlled. More details on the qcindex are available at: http://www.coaps.fsu.edu/RVSMDC/WOCE/qccodes_netcdf.shtml

| A | Original data had unknown units. The units shown were determined using a climatology or some other method. |
| --- | --- |
| B | Original data were out of physically realistic range bounds outlined. |
| C | Time data are not sequential or date/time not valid. |
| D | Data failed T≥Tw≥Td test. In the free atmosphere, the value of the temperature is always greater than or equal to the wet-bulb temperature, which in turn is always greater than or equal to the dew point temperature. |
| E | Data failed resultant wind re-computation check. When the data set includes the platform's heading, course, and speed along with the platform relative wind speed and direction, a program re-computes the earth relative wind speed and direction and compares the computed values to the reported earth relative wind speed and direction. A failed test occurs when the wind direction difference is > 20 degrees or the wind speed difference is >2.5m/s. |
| F | Platform velocity unrealistic. Determined by analyzing latitude and longitude positions as well as reported platform speed data. |
| G | Data are greater than 4 standard deviations from the COADS climatological means (da Silva et al. 1994). The test is only applied to pressure, temperature, sea temperature, relative humidity, and wind speed data. |
| H | Discontinuity found in data. |
| I | Interesting feature found in data. More specific information on the feature is contained in the data reports. Examples include: hurricanes passing stations, sharp seawater temperature gradients, strong convective events, etc. |
| J | Data are of poor quality by visual inspection, DO NOT USE. |
| K | Data suspect/use with caution – this flag applies when the data look to have obvious errors, but no specific reason for the error could be determined. |
| L | Oceanographic platform passes over land or fixed platform moves dramatically. |
| M | Known instrument malfunction. |
| N | Signifies that the data were collected while the vessel was in port. Typically these data, though realistic, are significantly different from open ocean conditions. |
| O | Original units differ from those listed in the original_units variable attribute. See quality control report for details. |
| P | Position of platform or its movement are uncertain. Data should be used with caution. |
| Q | Questionable - data arrived at DAC already flagged as questionable/uncertain. |
| R | Replaced with an interpolated value. Done prior to arrival at the DAC. Flag is used to note condition. Method of interpolation is often poorly documented. |
| S | Spike in the data. Usually one or two sequential data values (sometimes up to 4 values) that are drastically out of the current data trend. Spikes occur for many reasons including power surges, typos, data logging problems, lightning strikes, etc. |
| T | Time duplicate |
| U | Data failed statistical threshold test in comparison to temporal neighbors. This flag is output by automated Spike and Stair-step Indicator (SASSI) procedure developed by the DAC. |
| V | Data spike as determined by SASSI. |
| X | Step/discontinuity in data as determined by SASSI |
| Y | Suspect values between X-flagged data (from SASSI) |
| Z | Data passed evaluation. |